## Slide 1
  These slides contain animations, when the PowerPoint file is played
  The content gradually appears with clicks
  Questions appear before their answers

## Slide 2
Green Chemistry and Living in the Desert
Water
  Staying alive – drinking
  Clean water for drinking, what are the problems?
  How is water sterilized, chlorine, UV, ozone
  How is water purified? Distillation, reverse osmosis, deionization, charcoal.
  Drink containers - Recycling
  Cooling off – Swimming pool chemistry
  Chlorine, pH, buffers, water hardness
  Cleaning – detergents, dishwashing, laundry
  Biodegradation, algal blooms, eutrophication

## Slide 3
Cooling Off – Swimming Pools
Going for a swim is a great way to cool off!
What are some problems that a pool can have?
Chemistry plays a critical role in doing this
Keeping a swimming pool both safe and aesthetically pleasing requires careful maintenance of the water

## Slide 4
Cooling Off – Swimming Pools
Poor Appearance?
Dirt, leaves, insect bodies, other solids
Scale buildup
Green water
Corrosion of metal parts
Strong smell
What are some problems that a pool can have?
Safety/Effects on people?
Transmit disease
Burn eyes
Bleach hair/clothes
Turn hair green
Too cold/hot
Remedy
Filtration
Decrease dissolved salts
Chlorination
Balance pH
Chlorination
Chlorination
Balance pH
Chlorination
Chelating agent
Let’s look at some of these in more detail

## Slide 5
Swimming Pool Chemistry
Chlorination
Maintaining pool chemistry involves using chemicals to control the following:
pH
Buffer level
Stabilizer level
Dissolved salts/Water hardness
Algaecide
Water clarifier/flocculant
Copper remover
Phosphate remover
Some chemicals may need to be added less frequently:

## Slide 6
Swimming Pool Chemistry - Chlorination
Chlorine is a disinfectant
What does chlorine do?
The aim is to kill any organisms in the pool and to inactivate viruses
A relatively low level of chlorine in the water is quite effective at killing bacteria, parasites, fungi, algae, and destroying viruses without causing much problem for human swimmers
Other less commonly used disinfection methods include:
Bromine
Ozone
UV light
Hydrogen peroxide/UV light

## Slide 7
Swimming Pool Chemistry - Chlorination
Chlorine is a yellow-green gas! bp -34 °C
Chlorine (Cl2)
While chloride (Cl-) is necessary for all know species of life, chlorine (Cl2) is poisonous to most living organisms
So how are all these things “chlorine”?:
Wikipedia - chlorine
https://images.app.goo.gl/euFU3TK4k8XqtMrL6
https://images.app.goo.gl/g5nie2hbBK6CseaE6

## Slide 8
Swimming Pool Chemistry - Chlorination
Hypochlorous acid is in equilibrium with its dissociated form:
Chlorine reacts with water to form hypochlorous acid:
Cl2(g) + H2O ⇄ HOCl + H+ + Cl-
HOCl ⇄ + H+ + OCl-
Which species are present in water is highly dependent on pH
At pH 7.5 (typical pool pH) and 25 °C, the amounts of hypochlorous acid (HOCl) and hypochlorite ion (-OCl) are about equal
In strongly acidic water (low pH [~2]) chlorine is mostly present as dissolved Cl2
In basic water (pH > 8) chlorine is mostly present as hypochlorite ion (-OCl)

## Slide 9
Swimming Pool Chemistry - Chlorination
At pH 7.5 (typical pool pH) and 25 °C, the amounts of hypochlorous acid (HOCl) and hypochlorite ion (-OCl) are about equal
In strongly acidic water (low pH [~2]) chlorine is mostly present as dissolved Cl2
In basic water (pH > 8) chlorine is mostly present as hypochlorite ion (-OCl)
pH
-OCl
Cl2
HOCl + -OCl
The sanitizing effect is better when there is more HOCl/Cl2 present
However, Cl2 will escape at some rate from the system

## Slide 10
Swimming Pool Chemistry - Chlorination
So, what are these?:
This “Chlorine” is an aqueous solution of sodium hypochlorite (NaOCl)
Unlike calcium hypochlorite, it is not stable in solid form and is always used as a solution
This “Chlorine” is solid calcium hypochlorite (Ca(OCl)2)
Reaction with acid in the pool will generate HOCl, which is in equilibrium with Cl2

## Slide 11
Swimming Pool Chemistry - Chlorination
These tablets are made from trichloroisocyanuric acid
These react with acid to form chlorine (Cl2)
The same reaction occurs to release all three chlorines

## Slide 12
Swimming Pool Chemistry - Stabilizer
The reverse reaction of chlorine release can also occur to add Cl to isocyanuric acid
Cyanuric acid is added to the pool as a “stabilizer”, it reversibly binds some of the free chlorine, effectively giving a slower release, so giving a slower loss of chlorine

## Slide 13
Swimming Pool Chemistry - pH
However, when there is more Cl2 present in the water, it can leave the water as a gas and be lost
pH
-OCl
Cl2
HOCl + -OCl
This means the water should not be too basic (high pH) as it will lower the sanitizing power of the chlorine
Hypochlorite ion (-OCl) is not as effective at sanitizing as hypochlorous acid/chlorine
So, there is a balance between having a decent amount of “free” chlorine present and it being lost as a gas from the water, this is controlled by the pH

## Slide 14
Swimming Pool Chemistry - pH
pH
-OCl
Cl2
HOCl + -OCl
But the water can’t just be any pH, the swimmers will not tolerate the water if it is too basic or too acidic
When eye irritation occurs in a swimming pool the most likely cause is low pH (acidic). Human tears have pH ~7.0-7.4. That is a good target for the pool.
Low pH (acidic) also speeds corrosion of metal parts in the pool
https://images.app.goo.gl/9wa2qBCKq54bMmbZA

## Slide 15
Swimming Pool Chemistry - pH
How is pH adjusted?
Lower the pH – make it more acidic
Most commonly - add concentrated hydrochloric acid! Aka “muriatic acid”
Isn’t that dangerous?
Yes! Contact with skin will cause immediate burns, contact with eyes will cause catastrophic damage
Additionally, the fumes coming from concentrated HCl are noxious and corrosive
Safer solid acid sources such as NaHSO4 are also available, however they are generally much more expensive

## Slide 16
Swimming Pool Chemistry - pH
How is pH adjusted?
Increase the pH – make it more basic
Most commonly - add solid Na2CO3
Could add e.g. NaOH, but Na2CO3 is sufficiently basic and more easily handled, safer, and stable for storage

## Slide 17
Swimming Pool Chemistry - Buffer
A buffer is typically used with the pool water
Aka “total alkalinity” increaser
What is a buffer? Why is it used?
This is usually solid sodium bicarbonate (NaHCO3)
Adding a small amount of acid or base to the pool can cause a large swing in pH. Similarly, the pH can vary widely when the acid concentration changes for other reasons
A buffer helps to maintain a near constant pH, even when sizable amounts of acid or base are added:
CO32-  HCO3-  H2CO3
H+
-OH